## Slide 1: CUDA Thread Organization
Outline
CUDA -- BLOCKs of THREADs
MMM (again)
Granularity considerations
API-centric view
Interacting BLOCKs and THREADs
Notes: One of the major themes of this course is the interaction between hardware and software. We build hardware to run software, we analyze software/hardware interactions to improve hardware, we analyze software to best take advantage of hardware. It’s the last of these that we will examine now.
Of course once we’re done, then we can figure out how to build hw that improves this sw, but now we bring it to a higher level – we can parameterize the software so that it runs best on a wide variety of hardware (after all, even thought the sw implementation can change, the underlying application is probably fixed). Then we can build hardware that optimizes the parameterized code!
No, we’re not in Kansas anymore: this is obviously much more difficult than just looking at a bunch of benchmarks. However, before we get carried away, technological/programming constraints also constrain what we can do with the hardware, as we shall see.

## Slide 2
Technical specifications | Compute capability (version) |  |  |  |  |  |  |  |  | 
 | 1.0 | 1.1 | 1.2 | 1.3 | 2.x | 3.0 | 3.5 | 3.7 | 5.0 | 5.2
Maximum dimensionality of grid of thread blocks | 2 |  |  |  | 3 |  |  |  |  | 
Maximum x-dimension of a grid of thread blocks | 65535 |  |  |  |  | 231 − 1 |  |  |  | 
Maximum y-, or z-dimension of a grid of thread blocks | 65535 |  |  |  |  |  |  |  |  | 
Maximum dimensionality of thread block | 3 |  |  |  |  |  |  |  |  | 
Maximum x- or y-dimension of a block | 512 |  |  |  | 1024 |  |  |  |  | 
Maximum z-dimension of a block | 64 |  |  |  |  |  |  |  |  | 
Maximum number of threads per block | 512 |  |  |  | 1024 |  |  |  |  | 
Warp size | 32 |  |  |  |  |  |  |  |  | 
Maximum number of resident blocks per multiprocessor | 8 |  |  |  |  | 16 |  |  | 32 | 
Maximum number of resident warps per multiprocessor | 24 | 32 |  |  | 48 | 64 |  |  |  | 
Maximum number of resident threads per multiprocessor | 768 | 1024 |  |  | 1536 | 2048 |  |  |  | 
Number of 32-bit registers per multiprocessor | 8 K | 16 K |  |  | 32 K | 64 K |  | 128 K | 64 K | 
Maximum number of 32-bit registers per thread | 124 |  |  |  | 63 |  | 255 |  |  | 
Maximum amount of shared memory per multiprocessor | 16 KB |  |  |  | 48 KB |  |  | 112KB | 64KB | 96KB
Number of shared memory banks | 16 |  |  |  | 32 |  |  |  |  | 
Amount of local memory per thread | 16 KB |  |  |  | 512 KB |  |  |  |  | 
Constant memory size | 64 KB |  |  |  |  |  |  |  |  | 
Cache working set per multiprocessor for constant memory | 8 KB |  |  |  |  |  |  |  | 10 KB | 
TESLA
FERMI
KEPLER
MAXWELL
Wikipedia

## Slide 3
Arrays of Parallel Threads
A CUDA kernel is executed by an array of threads
  All threads run the same code (SIMT)‏
  Each thread has an ID that it uses to compute memory addresses and make control decisions
7
6
5
4
3
2
1
0
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
threadID
// Kernel definition - specified with __global__ syntax
__global__ void VecAdd (float* A, float* B, float* C)
{
int i = threadIdx.x; // get unique (1D) thread ID
C[i] = A[i] + B[i]; // do my bit of work
}
// Single block, but scales immediately to multiple blocks
int main()
{
…
// Kernel invocation
VecAdd<<<1,N>>>(A,B,C); // # of CUDA threads is specified
// with the <<<…>>> syntax

## Slide 4: Thread Blocks
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
threadID
Thread Block 0
…
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
Thread Block 1
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
Thread Block N - 1
Divide monolithic thread array into multiple blocks
Block  Instantiation of a kernel
  Block would be called a thread in a CPU!
Blocks contain some number of threads executing in SIMD
  Block instructions (executed by threads) are analogous to vector instructions
A Block is mapped to a single SM
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 5: Block Scheduling
Each block is an instantiation of a kernel and is analogous to a thread in Pthreads
In CUDA programs, generally lots of blocks are generated
Blocks run on exactly one SM
Some number of Blocks can run at the same time on an SM (up to 8 through Fermi)
There is no constraint on Block scheduling. Blocks can go in any order on any SM
Therefore, Blocks generally do not interact with each other!
block
block
block
block
block
block
block
block
SM
SM
SM
SM
SM
SM
SM
SM
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
bloc
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block
block

## Slide 6: Transparent Scalability
Hardware is free to assign blocks to any processor at any time
  A kernel scales across any number of parallel processors
Device
Block 7
Block 1
Block 4
Block 5
Block 6
Block 3
Block 2
Block 0
Kernel grid
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Device
Block 5
Block 1
Block 3
Block 4
Block 7
Block 6
Block 0
Block 2
Each block can execute in any order relative to other blocks.
time
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 7: Thread Blocks: Scalable Cooperation
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
threadID
Thread Block 0
…
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
Thread Block 1
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
Thread Block N - 1
Divide monolithic thread array into multiple blocks
  Why? This is purely hardware driven: it turns out that blocks are a good granularity of work (for DECOMPOSITION and ASSIGNMENT). A block is big enough to do real work on a single SM, but small enough to be worth creating in large numbers. The latter is important for scalability -- a large enough number of independent blocks can be mapped well onto 8 or 30 or 50 SMs!
  Threads within a block cooperate via shared memory, atomic operations, and barrier synchronization
  Threads in different blocks cannot cooperate. That’s right, THREADS IN DIFFERENT BLOCKS CANNOT COOPERATE!
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 8: Rules for Thread Organization – Fermi
THREADs are organized into BLOCKs:
Min(|THREADs|) / BLOCK = 1
Max(|THREADs|) / BLOCK = 1024
BLOCKs always run on a single SM
Multiple BLOCKs can run at the “same time” on a single SM:
Max(|BLOCKs|) / 1 SM = 8
Max(|BLOCKs|) / 14 SMs = 112
But the number of threads that can run on a SM is less than the product of the maxima:
Max(|THREADs|) / 1 SM = 1,536 >> not 8 x 1024 = 8,192
Max(|THREADs|) / 14 SMs = 21,504 >> not 14 x 8 x 1024 = 114,688
So 1536 THREADs (on a single SM) can be organized into:
  1 BLOCK of 1024 >> limit on # of threads/BLOCK
  3 BLOCKs of 512
  8 BLOCKs of 192 >> limit on # of BLOCKs

## Slide 9: Rules for Thread Organization, cont.
For multiple BLOCKs of THREADs, all BLOCKs must have the same size and shape.
  What’s “shape”? -- see on next slides
Why choose one organization over another? What should be …
… the Total Number of THREADs per problem?
  More THREADs means less work per THREAD
  Choosing this is another issue -- see below
… the Total Number of BLOCKs?
  More BLOCKs means less work per BLOCK
… the Number of THREADs per BLOCK?
  follows from other two
Total number of THREADs per SM depends on resources needed by each THREAD
must have sufficient available or else the THREAD launch will fail.
  note: this happens without error message, so be careful!
How many BLOCKs should those THREADs be organized into?

## Slide 10: BLOCK Shape
BLOCKs of THREADs can vary in SHAPE
  but not within a kernel launch
BLOCKs can have up to 3 dimensions
  Max(|THREADs|) / X Dimension = 1024
  Max(|THREADs|) / Y Dimension = 1024
  Max(|THREADs|) / Z Dimension = 64
Recall  Max(|THREADs|) / BLOCK = 1024
Syntax: Declare BLOCK shape as follows:
dim3 dimBlock(16,8,2); // dim3 declares a dimension specifier
// invoke kernel MatAdd with 1 BLOCK where that BLOCK has the shape
// specified by dimBLOCK
MatAdd<<<1, dimBlock>>>(A, B, C);

## Slide 11: More Rules for Thread Organization
BLOCKs are organized into a GRID
A GRID of BLOCKs can vary in SHAPE
From FERMI on, a GRID can also have 3 dimensions
  Max(|BLOCKs|) / X Dimension = 65535
  Max(|BLOCKs|) / Y Dimension = 65535
  Max(|BLOCKs|) / Z Dimension = 65535 (no Z in CUDA 1.x)
So we can be running a GRID with 281,462,092,005,375 blocks (2^48)
Q: But I thought we could only run 21,504 THREADs per 14 SMs?
A: Correct -- these BLOCKs are run sequentially. This is why THREADs in different BLOCKs can’t interact.
A: But there are also (obvious) system limitations that prevent programs with more than a small fraction of that number of BLOCKs from working. Example: size of system memory.

## Slide 12: Specifying GRIDs, etc.
Syntax: Declare GRID shape as follows:
dim3 dimGrid(4,4); // dim3 declares a dimension specifier,
// same as for THREADs in a BLOCK
dim3 dimBlock(16,16,1); // This time have 256 THREADs per BLOCK
// invoke kernel MatAdd with number of THREADs and BLOCK shape
// and GRID shape specified by dimGrid and dimBLOCK
MatAdd<<<dimGrid, dimBlock>>>(A, B, C);
// This declaration might make sense for processing arrays
// that are 64 x 64

## Slide 13: More on THREADs, BLOCKs, & GRIDs
Syntax: Find which THREAD or BLOCK you are as follows. These are all BUILT-IN VARIABLEs:
// Which THREAD in the X dimension (or Y or Z) of the BLOCK?
threadIdx.x, threadIdx.y, threadIdx.z // return the value
// Which BLOCK in the X dimension (or Y or Z) of the GRID?
blockIdx.x, blockIdx.y, blockIdx.z // return the value
------------------------------------------------------------------------------------------
Syntax: Find the number of THREADs in a BLOCK dimension:
// How many THREADs in the X dimension (or Y or Z) of the BLOCK?
blockDim.x, blockDim.y, BlockDim.z // return the value
// How many BLOCKs in the X dimension (or Y) of the GRID?
gridDim.x, gridDim.y, gridDim.z // return the value

## Slide 14: Example: THREADs, BLOCKs, GRIDs
__global__ void MatAdd(float A[64][64], float B[64][64],
float C[64][64])
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
int j = blockIdx.y * blockDim.y + threadIdx.y;
C[i][j] = A[i][j] + B[i][j];
}
int main()
{
…
// Kernel invocation
dim3 dimGrid(4,4); // 4x4 GRID of 16 BLOCKs
dim3 dimBLOCK(16,16,1); // 16x16 BLOCK of 256 THREADs per BLOCK
MatAdd<<<dimGrid, dimBlock>>>(A, B, C);
}

## Slide 15: Calling a Kernel Function – Thread Creation
A kernel function must be called with an execution configuration:
__global__ void KernelFunc(...);
dim3 DimGrid(100, 50); // 5000 thread blocks
dim3 DimBlock(4, 8, 8); // 256 threads per block
size_t SharedMemBytes = 64;// 64 bytes shared memory
KernelFunc<<< DimGrid, DimBlock, SharedMemBytes >>>(...);
Any call to a kernel function is asynchronous from CUDA 1.0 on, explicit CUDA synch needed for blocking
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 16: Block IDs and Thread IDs, review
Group BLOCKs into GRIDs
Each thread uses IDs to decide what data to work on
  Block ID: 1D, 2D, or 3D
  Thread ID: 1D, 2D, or 3D
Why? Simplifies memory addressing when processing multidimensional data
  Image processing
  Solving PDEs on volumes
  …
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 17: Lab 3
Goal: : Learn about blocks and threads.
Input: cuda_test_AI.cu, parametrized
Task: Vary definitions to try different numbers of blocks, threads/block, input sizes. Measure performance.

## Slide 18: 2. Ex: Matrix Multiplication Using Multiple Blocks
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTHE
WIDTH
WIDTH
Break-up Pd into tiles
Each block calculates one tile
  Each thread calculates one element
  Block size equal tile size
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 19: A Small Example: Multiplication
Pd1,0
Md2,0
Md1,1
Md1,0
Md0,0
Md0,1
Md3,0
Md2,1
Pd0,0
Md3,1
Pd0,1
Pd2,0
Pd3,0
Nd0,3
Nd1,3
Nd1,2
Nd1,1
Nd1,0
Nd0,0
Nd0,1
Nd0,2
Pd1,1
Pd0,2
Pd2,2
Pd3,2
Pd1,2
Pd3,1
Pd2,1
Pd0,3
Pd2,3
Pd3,3
Pd1,3
P1,0
P0,0
P0,1
P2,0
P3,0
P1,1
P0,2
P2,2
P3,2
P1,2
P3,1
P2,1
P0,3
P2,3
P3,3
P1,3
Block(0,0)
Block(1,0)
Block(1,1)
Block(0,1)
TILE_WIDTH = 2
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 20: Revised Matrix Multiplication Kernel using Multiple Blocks
// Single thread still does a single dot product,
// but within an output submatrix
__global__ void MatrixMulKernel(float* Md, float* Nd, float* Pd, int Width)
{
// Calculate the row index of the Pd element and M
// blockIdx.x gets ID within a block
int Row = blockIdx.y*TILE_WIDTH + threadIdx.y;
// Calculate the column index of Pd and N
int Col = blockIdx.x*TILE_WIDTH + threadIdx.x;
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += Md[Row*Width+k] * Nd[k*Width+Col];
Pd[Row*Width+Col] = Pvalue;
}

## Slide 21: Lab 4
Goal: Learn about MMM with multiple blocks
Input: MMM_global.cu, parametrized
Task: Vary code to change matrix size. Retain one thread per output. For same matrix size, see if it matters whether there are more blocks with fewer threads or vice versa.

## Slide 22: 3. Granularity Considerations CUDA Thread Block -- Review
All threads in a block execute the same kernel program (SIMT)
Programmer declares block:
  Block size 1 to 1024 concurrent threads
  Block shape 1D, 2D, or 3D
  Block dimensions in threads
All blocks in a grid (kernel invocation) have the same dimensions (shape)
Threads have thread id numbers within block
  Thread program uses thread id to select work and address shared data
Threads in the same block share data and synchronize while doing their share of the work
Threads in different blocks cannot cooperate
  Each block can execute in any order relative to other blocs!
CUDA Thread Block
Thread Id #: 0 1 2 3 … m
Thread program
Courtesy: John Nickolls, NVIDIA
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 23: GF100 Block Granularity Considerations
For Matrix Multiplication using multiple blocks, should I use 8X8, 16X16, 32X32, or 32X48 blocks?
  For 8X8, we have 64 threads per Block. Since each SM can take up to 1536 threads, there need to be 24 Blocks to reach thread capacity. However, each SM can only take up to 8 Blocks, only 512 threads will go into each SM.
  For 16X16, we have 256 threads per Block. Since each SM can take up to 1536 threads, it can take up to 6 Blocks and achieve full capacity unless other resource considerations overrule.
  For 32X32, we have 1024 threads per Block. This fits in both Block and SM, although does not use SM to thread capacity.
  For 32X48, we have 1536 threads per Block. Although this is allowed on the SM, it is too big for a BLOCK.
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 24
// MMM generalized so that threads potentially compute a number of output pixels rather
// than one as is assumed in the previous versions.
// This kernel assumes threads arranged as 2D blocks and blocks arranged as a 2D grid
__global__ void matrixMul(float* C, float* A, float* B, int row_a, int col_a, int col_b)
{
int i, j, k, m;
// Block index
const int bId_x = blockIdx.x;
const int bId_y = blockIdx.y;
// Local thread index
const int local_tid_x = threadIdx.x;
const int local_tid_y = threadIdx.y;
// Number of rows and columns of the result matrix to be evaluated by each block
const int rows_per_block = row_a / gridDim.x;
const int cols_per_block = col_b / gridDim.y;
const int rows_per_thread = rows_per_block / blockDim.x;
const int cols_per_thread = cols_per_block / blockDim.y;
// Row and column indices of the result matrix that the current block has to compute
const int blockStartId_row = bId_x * rows_per_block;
const int blockEndId_row = (bId_x+1) * rows_per_block - 1;
const int blockStartId_col = bId_y * cols_per_block;
const int blockEndId_col = (bId_y+1) * cols_per_block - 1;
const int threadStartId_row = blockStartId_row + local_tid_x * rows_per_thread;
const int threadEndId_row = blockStartId_row + (local_tid_x+1)* rows_per_thread - 1;
const int threadStartId_col = blockStartId_col + local_tid_y * cols_per_thread;
const int threadEndId_col = blockStartId_col + (local_tid_y+1)* cols_per_thread - 1;
int resultId;
float sum = 0;
for(i = threadStartId_row; i <= threadEndId_row; i++) {
for(j = threadStartId_col; j <= threadEndId_col; j++) {
sum = 0;
resultId = i*col_b + j;
for(k = 0; k < col_a; k++) {
sum = sum + A[i*col_a + k] * B[k*col_b + j];
}
C[resultId] = sum;
}
}
}
// Launching the kernel
dim3 my_block(block_dim_x, block_dim_y);
dim3 my_grid(grid_dim_x, grid_dim_y);
matrixMul<<<my_grid, my_block>>>(d_c, d_a, d_b, 8, 4, 12);

## Slide 25: MMM Examples
Can vary
-- number of BLOCKs
-- number of THREADs per BLOCK (1-1024, bounded by local SM memory)
-- amount of WORK per THREAD (bounded by local SM memory)
Assume 14 SMs
Max 1536 THREADs per SM (at a time)
Max 8 BLOCKs per SM (at a time)
Try a matrix size that fits in global memory: 8192x8192 (x8x3 ~= 1.61GB total)
-- BLOCK size = 32x32 = 1024
-- GRID size = 256x256 = 65,536 blocks
-- ~4681 BLOCKs per SM
Real questions
Is there any advantage to performing more work per THREAD?
What’s the best way to reuse data? From previous work, try to make inner ii,jj loops as big as possible.

## Slide 26: 4. Application Programming Interface
The API is an extension to the C programming language
It consists of:
  Language extensions
    To target portions of the code for execution on the device
  A runtime library split into:
    A common component providing built-in vector types and a subset of the C runtime library in both host and device codes
    A host component to control and access one or more devices from the host
    A device component providing device-specific functions
Language Extensions: Built-in Variables
dim3 gridDim;
  Dimensions of the grid in blocks
dim3 blockDim;
  Dimensions of the block in threads
dim3 blockIdx;
  Block index within the grid
dim3 threadIdx;
  Thread index within the block
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 27: Common Runtime Component: Mathematical Functions
pow, sqrt, cbrt, hypot
exp, exp2, expm1
log, log2, log10, log1p
sin, cos, tan, asin, acos, atan, atan2
sinh, cosh, tanh, asinh, acosh, atanh
ceil, floor, trunc, round
  When executed on the host, a given function uses the C runtime implementation if available
  These functions are only supported for scalar types, not vector types
Some mathematical functions (e.g. sin(x)) have a less accurate, but faster device-only version (e.g. __sin(x))
  __pow
  __log, __log2, __log10
  __exp
  __sin, __cos, __tan
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 28: Host Runtime Component
Provides functions to deal with:
  Device management (including multi-device systems)
  Memory management
  Error handling
Initializes the first time a runtime function is called
A host thread can invoke device code on only one device
  Multiple host threads required to run on multiple devices

## Slide 29: Device Runtime Component: Synchronization Function
void __syncthreads();
Synchronizes all threads in a block
Once all threads have reached this point, execution resumes normally
Used to avoid RAW / WAR / WAW hazards when accessing shared or global memory
Allowed in conditional constructs only if the conditional is uniform across the entire thread block
Notes: Atomic Operations?

## Slide 30: 5: Example – Simple THREAD/BLOCK interaction
The purpose of this example is to look at simple THREAD interaction under various scenarios. Assume 
Some number of SMs
Global memory only
Possibly multiple BLOCKs
Averaging filter
Input = 1D array with N elements
Output = 1D array with N elements
Operation – Each output array element is the average of its corresponding element in the input array and its neighbors.
Example: Average three neighbors.
A[i] = (A[i-1] + A[i] + A[i+1]) / 3
Correlation/Convolution are generalizations.
A[i] = w[0]*A[i-1] + w[1]*A[i] + w[2]*A[i+1]

## Slide 31: Example Parameters
Application  Averaging filter
Input = 1D array with N elements
Output = 1D array with N elements
Operation – Each output array element is the average of its corresponding element in the input array and its neighbors.
Example: Average three neighbors. Then A[i] = (A[i-1] + A[i] + A[i+1]) / 3
Correlation/Convolution are generalizations. A[i] = w[0]*A[i-1] + w[1]*A[i] + w[2]*A[i+1]
0. Read and Write Different/Same arrays.
N  B[i] = (A[i-1]+A[i]+A[i+1])/3
Y  A[i] = (A[i-1]+A[i]+A[i+1])/3
1. Many iterations or One iteration?
N  One iteration
Y  Many iterations
2. Many Blocks or One Block?
N  One BLOCK
Y  Many BLOCKs
8 Cases

## Slide 32
CASES 0-3 -- N(N/Y)(N/Y)
2. Single Block
1. One OR Many iterations
0. Same OR Different arrays
The first four cases are all Single Block.
The Single Block simplifies synchronization, but since it runs on a single SM, there is a restricted amount of SM memory to hold intermediate values and so both a limited number of threads and problem size.

## Slide 33
CASE 0 – NNN:
R/W different arrays
1 iteration
1 BLOCK
Easy: No sync needed.
__global__ void Average(float* A, float* B, int N)
{
int i = threadIdx.x;
if (i > 0 && i < N-1) // Not a FOR loop
B[i] = (A[i-1] + A[i] + A[i+1])/3;
}
// -------------------------------
int main()
{
…
// Kernel invocation
dim3 dimBlock(256,1,1);
Average<<<1, dimBlock>>>(A, B, 256);
}

## Slide 34
CASE 1 – NNY:
R/W same array
1 iteration
1 BLOCK
__global__ void Average(float* A, int N)
{
int i = threadIdx.x;
if (i > 0 && i < N-1) {
float X = (A[i-1] + A[i] + A[i+1])/3;
__syncthreads();
A[i] = X;
}
}
// ------------------
int main()
{
…
// Kernel invocation
dim3 dimBLOCK(256,1,1);
Average<<<1, dimBLOCK>>>(A, 256);
}
Must SYNC between reads and writes. Otherwise there is a race condition: some threads may read data that has already been written.

## Slide 35
CASE 2 – NYN:
R/W different arrays
Multiple iterations
1 BLOCK
__global__ void Average(float* A, float* B, int N)
{
int i = threadIdx.x;
for (int j = 0; j < 50; j++) {
if (i > 0 && i < N-1) {
B[i] = (A[i-1] + A[i] + A[i+1])/3;
__syncthreads();
A[i] = (B[i-1] + B[i] + B[i+1])/3;
__syncthreads();
}
}
}
// ------------------
int main()
{
…
// Kernel invocation
dim3 dimBlock(256,1,1);
Average<<<1, dimBlock>>>(A,B,256);
}
Must SYNC between writes. Otherwise there is a race condition: threads may be on different iterations and so read wrong data.

## Slide 36
CASE 3 – NYY:
R/W same array
Multiple iterations
1 BLOCK
__global__ void Average(float* A, int N)
{
int i = threadIdx.x;
for (int j = 0; j < 100; j++) {
if (i > 0 && i < N-1) {
float X = (A[i-1] + A[i] + A[i+1])/3;
__syncthreads();
A[i] = X;
__syncthreads();
}
}
}
// ------------------
int main()
{
…
// Kernel invocation
dim3 dimBlock(256,1,1);
Average<<<1, dimBlock>>>(A,256);
}
Must SYNC between reads and writes. Otherwise there is a race condition: threads may be on different iterations and so read wrong data.

## Slide 37
What’s the drawback of SYNCTHREADS?
At the end of the SYNC all activity must be completed, e.g., all writes by all threads in the BLOCK must have finished. This means that, if necessary, there must be enough space to hold all of these written intermediate values.
Why is this potentially a big deal? Let’s look at the CASE with a single array.
Code without SYNC looks like this:
A[i] = (A[i-1]+A[i]+A[i+1])/3
Code with SYNC looks like this:
x = (A[i-1]+A[i]+A[i+1])/3
SYNC
A[i] = x
The issue is not that there is an extra operation (involving x), this would be done anyway.
Rather it is that there must be a variable x available for each thread for the life of the kernel.
This also gives an idea about why there is a limit on the number of threads per BLOCK (although this is not the direct reason, that has to do with the number of contexts in the SMs).
If there are 1024 THREADs in a BLOCK and a BLOCK runs on a single SM, then there needs to be enough space on a single SM for all of the data being held by each of the 1024 THREADs.

## Slide 38
What about solving larger problems?
Q: What about problems where the array is bigger than the number of threads?
A: For array size N and number of THREADs T, each thread handles a number N/T output elements and N/T + 2 input elements (assuming padding at the very ends, which is also needed in the other case).
Q: What’s the difference whether there is just one array or multiple arrays (which swap)?
A:
With multiple arrays, this works fine as before: just SYNC after every write.
With a single array, you have to save a couple of values, but this works as well. The reason is that each THREAD need not save all of the intermediate values – it only needs to save the “boundary” elements to prevent a race condition.

## Slide 39
CASES 4-7 -- Y(N/Y)(N/Y)
2. Multiple Blocks
1. One OR Many iterations
0. Same OR Different arrays
With multiple BLOCKs, each BLOCK takes a part of the input/output arrays.
That means that for all cases--except single-iteration/different-arrays--there must be communication among BLOCKs.
This is because of the edge elements, that is, the elements on the left and right ends of the output array. For all cases except 5, these depend on the inputs of other BLOCKs.
The key factor is that BLOCKs are all completely independent: they can be scheduled to start and complete in any order. That means that you cannot SYNC among THREADs in different BLOCKs.

## Slide 40
CASE 4 – YNN:
R/W different arrays
1 iteration
Multiple BLOCKs
Easy: No sync needed
__global__ void Average(float A[N], float B[N])
{
int i = blockIdx.x * blockDim.x + threadIdx.x
if (i > 0 && i < N)
B[i] = (A[i-1] + A[i] + A[i+1])/3;
}
// ------------------
int main()
{
…
// Kernel invocation
dim3 dimGrid(16,1,1);
dim3 dimBlock(256,1,1);
Average<<<dimGrid, dimBLOCK>>>(A, B, 4096);
}

## Slide 41
CASES 5-7 – Y (NY|YN|YY)
R/W same array
single iteration
OR
R/W same array
multiple iterations
OR
R/W different arrays
multiple iterations
AND
Multiple BLOCKs
For all of these cases, Multiple BLOCKs means Multiple KERNEL LAUNCHES
Again, you cannot SYNC among THREADs in different BLOCKs
// CASE 5 -- Different Arrays, Multiple iterations
__global__ void Average1(float* A, float* B, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x
if (i > 0 && i < N-1)
B[i] = (A[i-1] + A[i] + A[i+1])/3;
}
__global__ void Average2(float A[N], float B[N])
{
int i = blockIdx.x * blockDim.x + threadIdx.x
if (i > 0 && i < N-1)
A[i] = (B[i-1] + B[i] + B[i+1])/3;
}
// ------------------
int main()
{
// Kernel invocations -- Since these are asynchronous,
// must force to launch all at once.
dim3 dimGrid(16,1,1);
dim3 dimBlock(256,1,1);
for (int i = 0; i < 50; i++) {
Average1<<<dimGrid, dimBlock>>>(A, B, N);
cudaDeviceSynchronize();
Average2<<<dimGrid, dimBlock>>>(A, B, N);
cudaDeviceSynchronize();
}
}
// cudaDeviceSynchronize()  Blocks until the device has completed all
// preceding requested tasks