## Slide 1: CUDA/GPU In Depth: Memory
Outline
Overview
Register File
Global Memory – coalescing
Notes: One of the major themes of this course is the interaction between hardware and software. We build hardware to run software, we analyze software/hardware interactions to improve hardware, we analyze software to best take advantage of hardware. It’s the last of these that we will examine now.
Of course once we’re done, then we can figure out how to build hw that improves this sw, but now we bring it to a higher level – we can parameterize the software so that it runs best on a wide variety of hardware (after all, even thought the sw implementation can change, the underlying application is probably fixed). Then we can build hardware that optimizes the parameterized code!
No, we’re not in Kansas anymore: this is obviously much more difficult than just looking at a bunch of benchmarks. However, before we get carried away, technological/programming constraints also constrain what we can do with the hardware, as we shall see.

## Slide 2
Technical specifications | Compute capability (version) |  |  |  |  |  |  |  |  | 
 | 1.0 | 1.1 | 1.2 | 1.3 | 2.x | 3.0 | 3.5 | 3.7 | 5.0 | 5.2
Maximum dimensionality of grid of thread blocks | 2 |  |  |  | 3 |  |  |  |  | 
Maximum x-dimension of a grid of thread blocks | 65535 |  |  |  |  | 231 − 1 |  |  |  | 
Maximum y-, or z-dimension of a grid of thread blocks | 65535 |  |  |  |  |  |  |  |  | 
Maximum dimensionality of thread block | 3 |  |  |  |  |  |  |  |  | 
Maximum x- or y-dimension of a block | 512 |  |  |  | 1024 |  |  |  |  | 
Maximum z-dimension of a block | 64 |  |  |  |  |  |  |  |  | 
Maximum number of threads per block | 512 |  |  |  | 1024 |  |  |  |  | 
Warp size | 32 |  |  |  |  |  |  |  |  | 
Maximum number of resident blocks per multiprocessor | 8 |  |  |  |  | 16 |  |  | 32 | 
Maximum number of resident warps per multiprocessor | 24 | 32 |  |  | 48 | 64 |  |  |  | 
Maximum number of resident threads per multiprocessor | 768 | 1024 |  |  | 1536 | 2048 |  |  |  | 
Number of 32-bit registers per multiprocessor | 8 K | 16 K |  |  | 32 K | 64 K |  | 128 K | 64 K | 
Maximum number of 32-bit registers per thread | 124 |  |  |  | 63 |  | 255 |  |  | 
Maximum amount of shared memory per multiprocessor | 16 KB |  |  |  | 48 KB |  |  | 112KB | 64KB | 96KB
Number of shared memory banks | 16 |  |  |  | 32 |  |  |  |  | 
Amount of local memory per thread | 16 KB |  |  |  | 512 KB |  |  |  |  | 
Constant memory size | 64 KB |  |  |  |  |  |  |  |  | 
Cache working set per multiprocessor for constant memory | 8 KB |  |  |  |  |  |  |  | 10 KB | 
TESLA
FERMI
KEPLER
MAXWELL

## Slide 3: Review: CUDA Device Memory Space
Each thread can:
  R/W per-thread registers
  R/W per-thread local memory
  R/W per-block shared memory
  R/W per-grid global memory
  Read only per-grid constant memory
  Read only per-grid texture memory
(Device) Grid
Constant
Memory
Texture
Memory
Global
Memory
Block (0, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Local
Memory
Thread (0, 0)
Registers
Local
Memory
Thread (1, 0)
Registers
Host
The host can R/W global, constant, and texture memories
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 4: Review: Parallel Memory – Data Sharing
Local Memory: per-thread
  Private per thread
  Auto variables, register spill
Shared Memory: per-Block
  Shared by threads of the same block
  Inter-thread communication
Global Memory: per-application
  Shared by all threads
  Inter-Grid communication
Thread
Local Memory
Grid 0
. . .
Global
Memory
. . .
Grid 1
Sequential
Grids
in Time
Block
Shared
Memory

## Slide 5: Review: SM Memory Architecture
Threads in a block share data & results
  In Memory and Shared Memory
  Synchronize at barrier instruction
Per-Block Shared Memory Allocation
  Keeps data close to processor
  Minimize trips to global Memory
  Shared Memory is dynamically allocated to blocks, one of the limiting resources
t0 t1 t2 … tm
Blocks
Texture L1
SP
Shared
Memory
MT IU
SP
Shared
Memory
MT IU
TF
L2
Memory
t0 t1 t2 … tm
Blocks
SM 1
SM 0
Courtesy:
John Nicols, NVIDIA

## Slide 6: Part 2: SM Register File
Register File (RF)
  128 KB (32K entries) for each SM in GF100
  Maximum registers per thread = 63
  Minimum registers per thread = 21
    With 1536 threads/SM, 32K/1536 = 21
TEX pipe can also read/write RF
  2 SMs share 1 TEX
Load/Store pipe can also read/write RF
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 7: Programmer View of Register File
There are 32K registers in each SM in GF100
  This is an implementation decision, not part of CUDA
  Registers are dynamically partitioned across all blocks assigned to the SM
  Once assigned to a block, the register is NOT accessible by threads in other blocks
  Each thread in the same block only access registers assigned to itself
  Block scheduler needs to know available resources
  # of registers must be statically determinable (?)
4 blocks
3 blocks
Limiting factors for # of blocks per SM:
# of blocks
# of threads
# of registers
size of shared mem

## Slide 8: G80 Matrix Multiplication Example
G80  8K registers, max threads = 1K, no lower limit on registers/thread
If each Block has 16X16 threads and each thread uses 10 registers, how many blocks can run on each SM?
  Each block requires 10*256 = 2560 registers
  8192 = 3 * 2560 + change
  So, three blocks can run on an SM as far as registers are concerned
How about if each thread increases the use of registers by 1?
  Each Block now requires 11*256 = 2816 registers
  8192 < 2816 *3
  Only two Blocks can run on an SM, 1/3 reduction of parallelism!!
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 9: More on Dynamic Partitioning
Dynamic partitioning gives more flexibility to compilers/programmers
  One can run a smaller number of threads that require many registers each or a large number of threads that require few registers each
    This allows for finer-grained threading than traditional CPU threading models.
  The compiler can trade off between instruction-level parallelism and (p)thread level parallelism

## Slide 10: G80 ILP vs. TLP Example
Assume that a kernel has
  Blocks with 256 Threads (8 Warps)
  4 independent instructions for each global memory load
  Each THREAD uses 10 registers
  Global loads take 200 cycles
  3 Blocks can run on each SM (24 warps)  4 Blocks require too many registers
Scenario: If a compiler can use one more register to change the dependence pattern so that 8 independent instructions exist for each global memory load
  Now only 2 blocks can run on each SM
  However, one only needs ceil[200/(8*4)] = 7 Warps to tolerate the memory latency
  Two blocks have 16 Warps. The performance can be actually higher!

## Slide 11: Part 3: Global Memory -- Performance Guidelines
Global memory instructions  4 byte, 8 byte, or 16 byte
  CUDA supports vector types of 2, 3, and 4 floats (and lots of other combinations)
  Variables should be aligned using __align__(8) or __align__(16)
Global memory bus in the GTX 285 has 512 bits (64 bytes, 16 words)
  and appears to have two banks
Global memory bandwidth is used most efficiently when the simultaneous memory accesses by THREADs in a HALF WARP (during the execution of a single read or write instruction) can be coalesced into a single memory transaction
  of 32, 64, or 128 bytes
  HALF WARP = 16 THREADs
  64 bytes for single precision
Global memory is partitioned into segments of the following sizes in bytes:
  32, 64, 128
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 12: Overview: Coalescing Global Memory Ops
Off-chip memory is accessed in chunks
  Even if you read only a single word
  If you don’t use whole chunk, bandwidth is wasted
Chunks are aligned to multiples of 32/64/128 bytes
  Unaligned accesses will cost more
Global memory access by all threads of a HALF-WARP (FULL-WARP in Fermi) is coalesced into a single transaction if the words accessed by all threads lie in the same segment of size
  32 bytes for 1-byte words
  64 bytes for 2-byte words
  128 bytes for 4- or 8-byte words
Coalescing is achieved for any pattern of addresses requested by the HALF-WARP, including where multiple THREADs access the same address.
Unused words in a memory transaction are still read, so they waste bandwidth.
HW will automatically issue the smallest memory transaction that contains the requested words.

## Slide 13: Coalescing, cont.
If a HALF-WARP addresses words in n different segments, then n memory transactions are issued.
Protocol:
Find the memory segment that contains the address requested by the lowest numbered active thread (not lowest address)
  32 bytes for 1-byte data, 64 bytes for 2-byte data, 128 bytes for 4-, 8- and 16-byte data
Find all other active threads whose requested addresses lie in the same segment
Reduce the transaction size, if possible:
  If the transaction is 128 (64) bytes and only the lower or upper half is used, reduce the transaction to 64 (32) bytes.
Carry out the transaction and mark the serviced threads
Repeat until all threads in the half-warp are serviced

## Slide 16: Threads 0-15 access 4-byte words at addresses 116-176
Thread 0 is lowest active, accesses address 116
128-byte segment: 0-127
96
192
128
128B segment
160
224
t1
t2
288
256
...
t0
t15
0
32
64
t3

## Slide 17: Threads 0-15 access 4-byte words at addresses 116-176
Thread 0 is lowest active, accesses address 116
128-byte segment: 0-127 (reduce to 64B)
96
192
128
64B segment
160
224
t1
t2
288
256
...
t0
t15
0
32
64
t3

## Slide 18: Threads 0-15 access 4-byte words at addresses 116-176
Thread 0 is lowest active, accesses address 116
128-byte segment: 0-127 (reduce to 32B)
96
192
128
32B transaction
160
224
t1
t3
288
256
...
t0
t15
0
32
64
t2

## Slide 19: Threads 0-15 access 4-byte words at addresses 116-176
Thread 3 is lowest active, accesses address 128
128-byte segment: 128-255
96
192
128
128B segment
160
224
t1
t2
288
256
...
t0
t15
0
32
64
t3

## Slide 20: Threads 0-15 access 4-byte words at addresses 116-176
Thread 3 is lowest active, accesses address 128
128-byte segment: 128-255 (reduce to 64B)
96
192
128
64B transaction
160
224
t1
t2
288
256
...
t0
t15
0
32
64
t3

## Slide 21: Consider the stride of your accesses
__global__ void foo(int* input, float3* input2)
{
int i = blockDim.x * blockIdx.x
+ threadIdx.x;
// Stride 1
int a = input[i];
// Stride 2, half the bandwidth is wasted
int b = input[2*i];
// Stride 3, 2/3 of the bandwidth wasted
float c = input2[i].x;
}

## Slide 22: Example: Array of Structures (AoS)
struct record
{
int key;
int value;
int flag;
};
record *d_records;
cudaMalloc((void**)&d_records, ...);

## Slide 23: Example: Structure of Arrays (SoA)
struct SoA
{
int * keys;
int * values;
int * flags;
};
SoA d_SoA_data;
cudaMalloc((void**)&d_SoA_data.keys, ...);
cudaMalloc((void**)&d_SoA_data.values, ...);
cudaMalloc((void**)&d_SoA_data.flags, ...);

## Slide 24: Example: SoA vs. AoS
__global__ void bar(record *AoS_data,
SoA SoA_data)
{
int i = blockDim.x * blockIdx.x
+ threadIdx.x;
// AoS wastes bandwidth
int key = AoS_data[i].key;
// SoA efficient use of bandwidth
int key_better = SoA_data.keys[i];
}

## Slide 25
Structure of arrays is often better than array of structures
  Very clear win on regular, stride 1 access patterns
  Unpredictable or irregular access patterns are case-by-case

## Slide 26: Review: Memory Layout of a Matrix in C
M2,0
M1,1
M1,0
M0,0
M0,1
M3,0
M2,1
M3,1
M2,0
M1,0
M0,0
M3,0
M1,1
M0,1
M2,1
M3,1
M1,2
M0,2
M2,2
M3,2
M1,2
M0,2
M2,2
M3,2
M1,3
M0,3
M2,3
M3,3
M1,3
M0,3
M2,3
M3,3
M

## Slide 27: Memory Coalescing
When accessing global memory, peak performance utilization occurs when all threads in a half warp access contiguous memory locations
Md
Nd
W
I
D
T
H
WIDTH
Thread 1
Thread 2
Not coalesced
coalesced
© David Kirk/NVIDIA and Wen-mei W. Hwu
Thread 1
Thread 2

## Slide 28: Memory Layout of a Matrix in C
M2,0
M1,1
M1,0
M0,0
M0,1
M3,0
M2,1
M3,1
M2,0
M1,0
M0,0
M3,0
M1,1
M0,1
M2,1
M3,1
M1,2
M0,2
M2,2
M3,2
M1,2
M0,2
M2,2
M3,2
M1,3
M0,3
M2,3
M3,3
M1,3
M0,3
M2,3
M3,3
M
T1
T2
T3
T4
Time Period 1
T1
T2
T3
T4
Time Period 2
Access direction in Kernel code
…
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 29: Memory Layout of a Matrix in C
M2,0
M1,1
M1,0
M0,0
M0,1
M3,0
M2,1
M3,1
M2,0
M1,0
M0,0
M3,0
M1,1
M0,1
M2,1
M3,1
M1,2
M0,2
M2,2
M3,2
M1,2
M0,2
M2,2
M3,2
M1,3
M0,3
M2,3
M3,3
M1,3
M0,3
M2,3
M3,3
M
T1
T2
T3
T4
Time Period 1
T1
T2
T3
T4
Time Period 2
Access direction in Kernel code
…
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 30: Review multiple block MMM – Are memory transfers coalesced?
// Single thread still does a single dot product,
// but within an output submatrix
__global__ void MatrixMulKernel(float* Md, float* Nd, float* Pd, int Width)
{
// Calculate the row index of the Pd element and M
// blockIdx.x gets ID within a block
int Row = blockIdx.y*TILE_WIDTH + threadIdx.y;
// Calculate the column index of Pd and N
int Col = blockIdx.x*TILE_WIDTH + threadIdx.x;
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += Md[Row*Width+k] * Nd[k*Width+Col];
Pd[Row*Width+Col] = Pvalue;
}

## Slide 31: Lab 5
Goal: : Learn about global memory reference patterns and their effect on performance
Input: MMM_global.cu
Task: Change code with loop interchange
Solution: MMM_global_ikj.cu