## Slide 1: CUDA Shared Memory
Outline
CUDA -- Shared Memory
Continue Example – MMM
Shared Memory Bank Conflicts
Continue Example -- Averaging Filter
Notes: One of the major themes of this course is the interaction between hardware and software. We build hardware to run software, we analyze software/hardware interactions to improve hardware, we analyze software to best take advantage of hardware. It’s the last of these that we will examine now.
Of course once we’re done, then we can figure out how to build hw that improves this sw, but now we bring it to a higher level – we can parameterize the software so that it runs best on a wide variety of hardware (after all, even thought the sw implementation can change, the underlying application is probably fixed). Then we can build hardware that optimizes the parameterized code!
No, we’re not in Kansas anymore: this is obviously much more difficult than just looking at a bunch of benchmarks. However, before we get carried away, technological/programming constraints also constrain what we can do with the hardware, as we shall see.

## Slide 2
Technical specifications | Compute capability (version) |  |  |  |  |  |  |  |  | 
 | 1.0 | 1.1 | 1.2 | 1.3 | 2.x | 3.0 | 3.5 | 3.7 | 5.0 | 5.2
Maximum dimensionality of grid of thread blocks | 2 |  |  |  | 3 |  |  |  |  | 
Maximum x-dimension of a grid of thread blocks | 65535 |  |  |  |  | 231 − 1 |  |  |  | 
Maximum y-, or z-dimension of a grid of thread blocks | 65535 |  |  |  |  |  |  |  |  | 
Maximum dimensionality of thread block | 3 |  |  |  |  |  |  |  |  | 
Maximum x- or y-dimension of a block | 512 |  |  |  | 1024 |  |  |  |  | 
Maximum z-dimension of a block | 64 |  |  |  |  |  |  |  |  | 
Maximum number of threads per block | 512 |  |  |  | 1024 |  |  |  |  | 
Warp size | 32 |  |  |  |  |  |  |  |  | 
Maximum number of resident blocks per multiprocessor | 8 |  |  |  |  | 16 |  |  | 32 | 
Maximum number of resident warps per multiprocessor | 24 | 32 |  |  | 48 | 64 |  |  |  | 
Maximum number of resident threads per multiprocessor | 768 | 1024 |  |  | 1536 | 2048 |  |  |  | 
Number of 32-bit registers per multiprocessor | 8 K | 16 K |  |  | 32 K | 64 K |  | 128 K | 64 K | 
Maximum number of 32-bit registers per thread | 124 |  |  |  | 63 |  | 255 |  |  | 
Maximum amount of shared memory per multiprocessor | 16 KB |  |  |  | 48 KB |  |  | 112KB | 64KB | 96KB
Number of shared memory banks | 16 |  |  |  | 32 |  |  |  |  | 
Amount of local memory per thread | 16 KB |  |  |  | 512 KB |  |  |  |  | 
Constant memory size | 64 KB |  |  |  |  |  |  |  |  | 
Cache working set per multiprocessor for constant memory | 8 KB |  |  |  |  |  |  |  | 10 KB | 
TESLA
FERMI
KEPLER
MAXWELL
Wikipedia

## Slide 3: Memory Hierarchy
CPU Main Memory
Device Memory
Shared Memory
8 GB/s for Fermi
100 GB/s
1000 GB/s
Constant Cache
Register Read
On-board
On-chip
SMs
On-chip shared memory is per SM.
   From Fermi on, there is also per-SM cache (L1) and global (L2) cache
Shared memories on different SMs are completely independent of one-another.
In fact, shared memory is partitioned by block and blocks can only access their own partitions of the shared memories on their own SMs
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 4: Memory Hierarchy (contd.)
CPU Main Memory
Device Memory
Shared Memory
Constant Cache
Before Fermi, device memory (Global) is not cached
Constant and Texture caches are read-only
Data must be brought into the shared memory by the threads
Shared memory is not persistent across “kernel” calls
Global, constant, and texture memory spaces are persistent across “kernel” calls
Shared memory on each SM is divided into 32 equally-sized banks that can be accessed simultaneously
Local memory is in Device Memory. It is called local because it is the per-thread “spill” storage
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 5: Programmer View of CUDA Memories
Each thread can:
  Read/write per-thread registers (~1 cycle)
  Read/write per-thread local memory (sits in global memory ~100s of cycles)
  Read/write per-block shared memory (~5 cycles)
  Read/write per-grid global memory (~500 cycles)
  Read/only per-grid constant memory (~5 cycles with caching)
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
L1 Cache
L2 Cache
 not programmer visible
© David Kirk/NVIDIA and Wen-mei W. Hwu
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 6: CUDA Variable Type Qualifiers
__device__ is optional when used with __local__, __shared__, or __constant__
“automatic” scalar variables without qualifier reside in a register
  compiler will spill to thread local memory
“automatic” array variables without qualifier reside in thread-local memory
Variable declaration | Memory | Scope | Lifetime
int var; | register | thread | thread
int array_var[10]; | local | thread | thread
__shared__ int shared_var; | shared | block | block
__device__ int global_var; | global | grid | application
__constant__ int constant_var; | constant | grid | application
© David Kirk/NVIDIA and Wen-mei W. Hwu
Notes: “automatic” refers to C variables which have resources automatically assigned to them by the compiler
The compiler has the discretion to put statically-indexed arrays into registers

## Slide 7: CUDA Variable Type Performance
scalar variables reside in fast, on-chip registers
shared variables reside in fast, on-chip memories
thread-local arrays & global variables reside in uncacheable off-chip memory
constant variables reside in cacheable off-chip memory
Variable declaration | Memory | Penalty
int var; | register | 1x
int array_var[10]; | local | 100x
__shared__ int shared_var; | shared | 1x
__device__ int global_var; | global | 100x
__constant__ int constant_var; | constant | 1x
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 8: CUDA Variable Type Scale
100Ks per-thread variables, R/W by 1 thread
100s shared variables, each R/W by 100s of threads
1 global variable is R/W by 100Ks threads
1 constant variable is readable by 100Ks threads
Variable declaration | Instances | Visibility
int var; | 100,000s | 1
int array_var[10]; | 100,000s | 1
__shared__ int shared_var; | 100s | 100s
__device__ int global_var; | 1 | 100,000s
__constant__ int constant_var; | 1 | 100,000s
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 9: Where to declare variables?
Can host access it?
Outside of any function
In the kernel
Yes
No
__constant__ int constant_var;
__device__ int global_var;
int var;
int array_var[10];
__shared__ int shared_var;
register (automatic)
shared
local
global
constant
texture
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 10: Variable Type Restrictions
Pointers can only point to memory allocated or declared in global memory:
  Allocated in the host and passed to the kernel:
  __global__ void KernelFunc(float* ptr)
  Obtained as the address of a global variable:
  float* ptr = &GlobalVar;

## Slide 11: Programming Strategy
Constant memory also resides in device memory (DRAM) - much slower access than shared memory
  But… cached!
  Highly efficient access for read-only data
Carefully divide data according to access patterns
  R/Only  constant memory (very fast if in cache)
  R/W shared within Block  shared memory (very fast)
  R/W within each thread  registers (very fast)
  R/W inputs/results  global memory (very slow)
  R/W shared not within a Block  global memory (very slow)
For texture memory usage, see NVIDIA document.

## Slide 12: Programming Strategy, cont.
A profitable way of performing computation on the device is to tile data to take advantage of fast shared memory:
  Partition data into subsets that fit into shared memory
  Handle each data subset with one thread block by:
    Loading the subset from global memory to shared memory, using multiple threads to exploit memory-level parallelism
    Performing the computation on the subset from shared memory; each thread can efficiently multi-pass over any data element
    Copying results from shared memory to global memory

## Slide 13: Shared Memory in CUDA
A special type of memory whose contents are explicitly declared and used in the source code
  Located in the processor
  Accessed at much higher speed (in both latency and throughput)
  Still accessed by memory access instructions
Shared Memory can be viewed as explicitly managed cache
  In computer architecture this is sometimes referred to as Scratchpad Memory
  Unlike cache, scratchpad does not necessarily hold a copy of data that is also in main memory
  It requires explicit data transfer instructions, whereas cache doesn’t

## Slide 14: Shared Memory -- Summary (from text)
The scope of a shared variable is within a thread BLOCK
  That is, all threads in a block see the same version of a shared variable.
A private version of the shared variable is created for, and used by, each thread BLOCK during kernel execution
The lifetime of a shared variable is the duration of the kernel
  When a kernel terminates, its shared variables cease to exist.
Shared variables are an efficient means for threads within a block to collaborate with each other
Accessing shared memory is extremely fast and highly parallel
  CUDA programmers often use shared memory to hold the portion of global memory data that is heavily used.
  One may need to adjust the algorithms used in order to create execution phases that heavily focus on small portions of the global memory data.
    see matrix multiplication (next)

## Slide 15: Matrix Multiplication using Shared Memory

## Slide 16: Review: Matrix Multiplication Using Multiple Blocks
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTHE
WIDTH
WIDTH
Break-up Pd into tiles
Each block calculates one tile
  Each thread calculates one element
  Block size equal tile size

## Slide 17: Review: Matrix Multiplication Kernel using Multiple Blocks
__global__ void MatrixMulKernel(float* Md, float* Nd, float* Pd, int Width)
{
// Calculate the row index of the Pd element and M
int Row = blockIdx.y*TILE_WIDTH + threadIdx.y;
// Calculate the column index of Pd and N
int Col = blockIdx.x*TILE_WIDTH + threadIdx.x;
float Pvalue = 0; // register
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += Md[Row*Width+k] * Nd[k*Width+Col];
Pd[Row*Width+Col] = Pvalue;
}

## Slide 18: How about performance on Fermi?
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
All threads access global memory for their input matrix elements
  Two memory accesses (8 bytes) per floating point multiply-add
  4B/s of memory bandwidth/FLOPS
  4*1,000 = 4,000 GB/s required to achieve peak FLOP rating
  150 GB/s limits the code at 37.5 GFLOPS
The actual code runs at about 25 GFLOPS
Need to drastically cut down memory accesses to get closer to the peak 1,000 GFLOPS

## Slide 19: Idea: Use Shared Memory to reuse global memory data
Each input element is read by Width threads
Load each element into Shared Memory and have several threads use the local version to reduce the memory bandwidth
  Tiled algorithms
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
ty
tx

## Slide 20: Tiled Multiply
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Break up the execution of the kernel into phases so that the data accesses in each phase are focused on one subset (tile) of Md and Nd
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 21: A Small Example
Pd1,0
Md2,0
Md1,1
Md1,0
Md0,0
Md0,1
Md3,0
Md2,1
Pd0,0
Md3,1
Pd0,1
Pd2,0
Pd3,0
Nd0,3
Nd1,3
Nd1,2
Nd1,1
Nd1,0
Nd0,0
Nd0,1
Nd0,2
Pd1,1
Pd0,2
Pd2,2
Pd3,2
Pd1,2
Pd3,1
Pd2,1
Pd0,3
Pd2,3
Pd3,3
Pd1,3
// Let 1 BLOCK compute one 2x2 output tile
// Unroll loop to make reuse obvious
P00 += M00 * N00
P00 += M10 * N01
P00 += M20 * N02
P00 += M30 * N03
P10 += M00 * N10
P10 += M10 * N11
P10 += M20 * N12
P10 += M30 * N13
P01 += M01 * N00
P01 += M11 * N01
P01 += M21 * N02
P01 += M31 * N03
P11 += M01 * N10
P11 += M11 * N11
P11 += M21 * N12
P11 += M31 * N13
// How much reuse is there?
// What can prevent reuse from being useful?
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 22: Every Md and Nd Element is used exactly twice in generating a 2X2 tile of P
P0,0 thread0,0 | P1,0 thread1,0 | P0,1 thread0,1 | P1,1 thread1,1
M0,0 * N0,0 | M0,0 * N1,0 | M0,1 * N0,0 | M0,1 * N1,0
M1,0 * N0,1 | M1,0 * N1,1 | M1,1 * N0,1 | M1,1 * N1,1
M2,0 * N0,2 | M2,0 * N1,2 | M2,1 * N0,2 | M2,1 * N1,2
M3,0 * N0,3 | M3,0 * N1,3 | M3,1 * N0,3 | M3,1 * N1,3
Access
order
© David Kirk/NVIDIA and Wen-mei W. Hwu
done in parallel

## Slide 23: Breaking Md and Nd into Tiles
Pd1,0
Md2,0
Md1,1
Md1,0
Md0,0
Md0,1
Md3,0
Md2,1
Pd0,0
Md3,1
Pd0,1
Pd2,0
Pd3,0
Nd0,3
Nd1,3
Nd1,2
Nd1,1
Nd1,0
Nd0,0
Nd0,1
Nd0,2
Pd1,1
Pd0,2
Pd2,2
Pd3,2
Pd1,2
Pd3,1
Pd2,1
Pd0,3
Pd2,3
Pd3,3
Pd1,3
// Let 1 BLOCK compute one 2x2 output tile
// This time, group by input tile
// Unroll loop to make reuse obvious
P00 += M00 * N00
P00 += M10 * N01
P10 += M00 * N10
P10 += M10 * N11
P01 += M01 * N00
P01 += M11 * N01
P11 += M01 * N10
P11 += M11 * N11
P00 += M20 * N02
P00 += M30 * N03
P10 += M20 * N12
P10 += M30 * N13
P01 += M21 * N02
P01 += M31 * N03
P11 += M21 * N12
P11 += M31 * N13
// How much reuse is there?
// Which thread executes which instructions?
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 24
// Let 1 BLOCK compute one 2x2 output tile
// How do you load the data?
// There are 4 threads
// For 1 block, each “phase” (tile) use
// 4 M elements (input) M00, M01, M10, M11
// 4 N elements (input) N00, N01, N10, N11
// 4 P elements (output) P00, P01, P10, P11
// Which thread loads which elements?

## Slide 25: Each phase of a Thread Block uses one tile from Md and one from Nd
 |  |  |  | Step 4 | Step 5 | Step 6
T0,0 | Md0,0 ↓ Mds0,0 | Nd0,0 ↓ Nds0,0 | PValue0,0 += Mds0,0*Nds0,0 + Mds1,0*Nds0,1 | Md2,0 ↓ Mds0,0 | Nd0,2 ↓ Nds0,0 | PValue0,0 += Mds0,0*Nds0,0 + Mds1,0*Nds0,1
T1,0 | Md1,0 ↓ Mds1,0 | Nd1,0 ↓ Nds1,0 | PValue1,0 += Mds0,0*Nds1,0 + Mds1,0*Nds1,1 | Md3,0 ↓ Mds1,0 | Nd1,2 ↓ Nds1,0 | PValue1,0 += Mds0,0*Nds1,0 + Mds1,0*Nds1,1
T0,1 | Md0,1 ↓ Mds0,1 | Nd0,1 ↓ Nds0,1 | PdValue0,1 += Mds0,1*Nds0,0 + Mds1,1*Nds0,1 | Md2,1 ↓ Mds0,1 | Nd0,3 ↓ Nds0,1 | PdValue0,1 += Mds0,1*Nds0,0 + Mds1,1*Nds0,1
T1,1 | Md1,1 ↓ Mds1,1 | Nd1,1 ↓ Nds1,1 | PdValue1,1 += Mds0,1*Nds1,0 + Mds1,1*Nds1,1 | Md3,1 ↓ Mds1,1 | Nd1,3 ↓ Nds1,1 | PdValue1,1 += Mds0,1*Nds1,0 + Mds1,1*Nds1,1
Phase 1
Phase 2
time
done in parallel
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 26: Review – Loading a Tile
All threads in a block participate
  Each thread loads one Md element and one Nd element in based tiled code
Assign the loaded element to each thread such that the accesses within each warp is coalesced (more later).

## Slide 27: Review – Work for Block (0,0), 1st tile
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
SM
SM
Four threads in parallel
Fetch 4 elements from 1st input tile of 1st input (1/thread)
Fetch 4 elements from 1st input tile of 2nd input (1/thread)

## Slide 28
SM
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
Four threads in parallel compute
1st MADD for each element of output tile (1/thread)

## Slide 29
SM
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
Four threads in parallel compute
2nd MADD for each element of output tile (1/thread)

## Slide 30: Review – Work for Block (0,0), 2nd tile
N1,0
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,1
SM
SM
Four threads in parallel
Fetch 4 elements from 2nd input tile of 1st input (1/thread)
Fetch 4 elements from 2nd input tile of 2nd input (1/thread)

## Slide 31
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
SM
Four threads in parallel compute
3rd MADD for each element of output tile (1/thread)

## Slide 32
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
SM
Four threads in parallel compute
4th MADD for each element of output tile (1/thread)

## Slide 33: First-order Size Considerations
Each thread block should have many threads
  TILE_WIDTH of 16 gives 16*16 = 256 threads
  TILE_WIDTH of 32 gives 32*32 = 1024 threads
There should be many thread blocks
  For 16, a 1024*1024 Pd gives 64*64 = 4096 Thread Blocks
For 16, each block performs 2*256 = 512 float loads from global memory for 256 * (2*16) = 8,192 mul/add operations.
For 32, each block performs 2*1024 = 2048 float loads from global memory for 1024 * (2*32) = 65,536 mul/add operations

## Slide 34: CUDA Code – Kernel Execution Config
// Set up the execution configuration
dim3 dimBlock(TILE_WIDTH, TILE_WIDTH);
dim3 dimGrid(Width / TILE_WIDTH,
Width / TILE_WIDTH);

## Slide 35: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* Md, float* Nd, float* Pd, int Width)
{
__shared__float Mds[TILE_WIDTH][TILE_WIDTH]; // Shared memory
__shared__float Nds[TILE_WIDTH][TILE_WIDTH]; // declarations
int bx = blockIdx.x; int by = blockIdx.y; // ID thread
int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the Pd element to work on
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0; // REGISTER!
// Loop over the Md and Nd tiles required to compute the Pd element
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Collaborative loading of Md and Nd tiles into shared memory
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__syncthreads();
}
Pd[Row*Width+Col] = Pvalue;
}

## Slide 36: Tiled Multiply
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Each block computes one square sub-matrix Pdsub of size TILE_WIDTH
Each thread computes one element of Pdsub
m
k
bx
by
k
m
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 37: Lab 6
Goal: Learn about shared memory
Input: MMM_shared.cu, parametrized
Task: Change the tile size and threads per block and number of blocks.

## Slide 38: Shared Memory, Threading, Reuse
Each SM in Fermi has 16KB or 48KB shared memory*
  SM size is GPU and configuration dependent!
  For TILE_WIDTH = 16, each thread block uses 2*256*4B = 2KB of shared memory.
  Can potentially have up to 8 Thread Blocks actively executing
    This allows up to 8*512 = 4,096 pending loads. (2 per thread, 256 threads per block)
  The next TILE_WIDTH 32 would lead to 2*32*32*4B= 8KB shared memory usage per thread block, allowing 2 or 6 thread blocks active at the same time
Using 16x16 tiling, we reduce the accesses to the global memory by a factor of 16
  The 86.4GB/s bandwidth can now support (86.4/4)*16 = 347.6 GFLOPS!
Reuse: Let TILE_WIDTH = B (as before)
Each tile multiply requires 2xB2 loads and B3 MADDs
Reuse = B/2
Example: 2x2 blocks  8 multiplies (2/thread), 8 loads (2/thread)
*Configurable vs L1, total 64KB

## Slide 39: Tiling Size Effects (G80 study)
Notes: Mention that we’re limited from large tile sizes by thread context maximums.

## Slide 40
for (i=0; i<N; i=i+B)
for (j=0; j<N; j=i+B)
for (k=0; k<N; k=k+B)
for (ii=i; ii<i+B; ii=ii+1)
for (jj=j; jj<j+B; jj=jj+1)
for (kk=k; kk<k+B; kk=kk+1)
x[ii][jj] = y[ii][kk] * z[kk][jj];
What is each THREAD computing?
What is each BLOCK computing?
NxN THREADs
3 x 3 = 9 BLOCKs
NxN/9 = THREADs/BLOCK
Inner loop of each THREAD = kk loop
THREADs within BLOCK = ii,jj loops
Different phases within THREAD = k loop
Different BLOCKs = i, j loops
kk
kk
P
ii
jj
M
N
P
k
k
i
j

## Slide 41: Part 4: Shared Memory Banks
Each SM has 16-48 KB of Shared Memory
  32 banks of 32-bit words
CUDA uses Shared Memory as shared storage visible to all threads in a thread block
  read and write access
Not used explicitly for pixel shader programs
  we dislike pixels talking to each other 
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 42: In General: Parallel Memory Architecture
In a parallel machine, many threads access memory
  Therefore, memory is divided into banks
  Essential to achieve high bandwidth
Each bank can service one address per cycle
  A memory can service as many simultaneous accesses as it has banks
Multiple simultaneous accesses to a bank result in a bank conflict
  Conflicting accesses are serialized
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 43: Bank Addressing Examples
No Bank Conflicts
  Linear addressing stride == 1
No Bank Conflicts
  Random 1:1 Permutation
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 44: Bank Addressing Examples
2-way Bank Conflicts
  Linear addressing stride == 2
8-way Bank Conflicts
  Linear addressing stride == 8
Thread 11
Thread 10
Thread 9
Thread 8
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 9
Bank 8
Bank 15
Bank 7
Bank 2
Bank 1
Bank 0
x8
x8
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 45: Bank Addressing Examples
16-way Bank NON-Conflict
  Linear addressing stride == 16
  This is now a broadcast
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 9
Bank 8
Bank 15
Bank 7
Bank 2
Bank 1
Bank 0
x16
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 46: How addresses map to banks on G80
Each bank has a bandwidth of 32 bits per clock cycle
Successive 32-bit words are assigned to successive banks
GF100 has 32 banks (Tesla had 16)
  So bank = address % 32
  Same as the size of a warp (previously half-warp)
    No bank conflicts between different warps, only within a single warp
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 47: Shared memory bank conflicts
Shared memory is as fast as registers if there are no bank conflicts
The fast cases:
  If all threads of a warp access different banks, there is no bank conflict
  If all threads of a warp access the identical address, there is no bank conflict (broadcast)
The slow case:
  Bank Conflict: multiple threads in the same warp access the same bank
  Must serialize the accesses
  Cost = max # of simultaneous accesses to a single bank
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 48: Linear Addressing
Given:
__shared__ float shared[256];
float foo = shared[baseIndex +
s * threadIdx.x];
This is only bank-conflict-free if s shares no common factors with the number of banks
  16 on G80, so s must be odd
  32 on GF100
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 15
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 15
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
s=3
s=1
© David Kirk/NVIDIA and Wen-mei W. Hwu

## Slide 49: Strided Example -- Tiled MMM
__global__ void MatrixMulKernel(float* Md, float* Nd, float* Pd, int Width)
{
__shared__float Mds[TILE_WIDTH][TILE_WIDTH]; // Shared memory
__shared__float Nds[TILE_WIDTH][TILE_WIDTH]; // declarations
int bx = blockIdx.x; int by = blockIdx.y; // ID thread
int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the Pd element to work on
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0; // REGISTER!
// Loop over the Md and Nd tiles required to compute the Pd element
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Collaborative loading of Md and Nd tiles into shared memory
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
Synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}

## Slide 50: Putting It Together: Global Memory Coalescing and Bank Conflicts
Let’s look at matrix transpose
Simple goal: Replace A[i][j] with A[j][i]
Any reuse of data?
Do you think shared memory might be useful?

## Slide 51: Matrix Transpose (from SDK)
_global__ void transpose(float *odata, float *idata, int width, int height)
{
// read the element
unsigned int xIndex = blockIdx.x * BLOCK_DIM + threadIdx.x;
unsigned int yIndex = blockIdx.y * BLOCK_DIM + threadIdx.y;
unsigned int index_in = yIndex * width + xIndex;
temp = idata[index_in];
// write the transposed element to global memory
xIndex = blockIdx.y * BLOCK_DIM + threadIdx.y;
yIndex = blockIdx.x * BLOCK_DIM + threadIdx.x;
unsigned int index_out = yIndex * height + xIndex;
odata[index_out] = temp;
}
odata and idata in global memory

## Slide 52: Coalesced Matrix Transpose
_global__ void
transpose(float *odata,float *idata,int width,int height)
{
__shared__ float block[BLOCK_DIM][BLOCK_DIM];
// read the matrix tile into shared memory
unsigned int xIndex = blockIdx.x * BLOCK_DIM + threadIdx.x;
unsigned int yIndex = blockIdx.y * BLOCK_DIM + threadIdx.y;
unsigned int index_in = yIndex * width + xIndex;
block[threadIdx.y][threadIdx.x] = idata[index_in];
__syncthreads();
// write the transposed matrix tile to global memory
xIndex = blockIdx.y * BLOCK_DIM + threadIdx.x;
yIndex = blockIdx.x * BLOCK_DIM + threadIdx.y;
unsigned int index_out = yIndex * height + xIndex;
odata[index_out] = block[threadIdx.x][threadIdx.y];
}
odata and idata in global memory
Rearrange in shared memory and write back efficiently to global memory

## Slide 53: Further Optimization: Partition Camping
A further optimization improves bank conflicts in global memory
    But has not proven that useful in codes with additional computation
Map blocks to different parts of chips
  int bid = blockIdx.x + gridDim.x*blockIdx.y;
  by = bid%gridDim.y;
  bx = ((bid/gridDim.y)+by)%gridDim.x;

## Slide 54: Performance Results for Matrix Transpose (GTX280)
SDK-prev: all optimizations other than partition camping
CHiLL: generated by our compiler
SDK-new: includes partition camping

## Slide 55: Continue example: Simple THREAD/BLOCK interaction

## Slide 56: Continue Example
The purpose of this example is to look at simple THREAD interaction under various scenarios. Assume 
Some number of SMs
Possibly multiple BLOCKs
Global Memory and SM Shared Memory
Averaging filter
Input = 1D array with N elements
Output = 1D array with N elements
Operation – Each output array element is the average of its corresponding element in the input array and its neighbors.

## Slide 57: Example Parameters
Averaging filter
Input = 1D array with N elements
Output = 1D array with N elements
Operation – Each output array element is the average of its corresponding element in the input array and its neighbors.
0. Read and Write Different/Same arrays.
N  B[i] = (A[i-1]+A[i]+A[i+1])/3
Y  A[i] = (A[i-1]+A[i]+A[i+1])/3
1. Many iterations or One iteration?
N  One iteration
Y  Many iterations
2. Many Blocks or One Block?
N  One BLOCK
Y  Many BLOCKs
3. Shared Memory or Global Memory Only?
N  Global Memory Only
Y  Shared Memory and Global Memory
16 Cases

## Slide 58
CASES 8-15 -- Y(N/Y)(N/Y)(N/Y)
Use Shared Memory as well as Global Memory
For Shared Memory, single iteration makes no sense – this is just a useless copy operation. So no CASES 8,9,12,13
CASES 10,11,14,15 -- Y(N/Y)Y(N/Y)
3. Shared Memory and Global Memory
2. Single OR Many Blocks
1. Many iterations
0. Same OR Different arrays

## Slide 59
CASE 10 (CASE 11 is similar)
3. Shared and Global Memory
2. Single Block
1. Multiple Iterations
0. Different Arrays (same array)
Note: Transfer data from global memory to shared and then back again when done.
Note: Shared memory arrays need to have a fixed size known at kernel launch time.
(check this -- maybe not necessarily)
#define threadN 256
__global__ void Average(float* A, float* B, int N)
{ // start by getting the number of threads in BLOCK
int i = threadIdx.x; // who am I?
__shared__float Ads[threadN];
__shared__float Bds[threadN];
// transfer data from global to shared memory
Ads[i] = A[i]; // each thread, coalesced
Bds[i] = B[i];
__syncthreads();
// do averaging
for (int j = 0; j < 50; j++) {
if (i > 0 && i < threadN-1) {
Bds[i] = (Ads[i-1] + Ads[i] + Ads[i+1])/3;
__syncthreads();
Ads[i] = (Bds[i-1] + Bds[i] + Bds[i+1])/3;
__syncthreads();
}
}
// transfer data from shared to global memory
__syncthreads();
A[i] = Ads[i];
B[i] = Bds[i];
}
int main()
{ …
// Kernel invocation
dim3 dimBlock(256,1,1);
Average<<<1, dimBlock>>>(A,B,256);
}

## Slide 60
CASE 14 (CASE 15 is similar)
3. Shared and Global Memory
2. Multiple Blocks
1. Multiple Iterations
0. Different Arrays (same array)
First recall the Global-Memory-Only CASE 5 (at right ). Kernels are spawned only for a single operation.
This is obviously no good for Shared Memory:
Shared Memory is LOST across kernel calls.
// CASE 5 -- Different Arrays, Multiple iterations
__global__ void Average1(float* A, float* B, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x
if (i > 0 && i < N-1)
B[i] = (A[i-1] + A[i] + A[i+1])/3;
}
__global__ void Average2(float A[N], float B[N])
{
int i = blockIdx.x * blockDim.x + threadIdx.x
if (i > 0 && i < N-1)
A[i] = (B[i-1] + B[i] + B[i+1])/3;
}
int main()
{
// Kernel invocations -- Since these are
// asynchronous, must force to launch all at once.
dim3 dimGrid(16,1,1);
dim3 dimBlock(256,1,1);
for (int i = 0; i < 50; i++) {
Average1<<<dimGrid, dimBlock>>>(A, B, N);
cudaThreadSynchronize();
Average2<<<dimGrid, dimBlock>>>(A, B, N);
cudaThreadSynchronize();
}
}
// cudaThreadSynchronize()  Blocks until the device has completed
// all preceding requested tasks

## Slide 61
CASE 14 (CASE 15 is similar)
3. Shared and Global Memory
2. Multiple Blocks
1. Multiple Iterations
0. Different Arrays (same array)
PROBLEM: Each THREAD must communicate with its neighbors.
With ONE BLOCK, that’s OK, use normal SYNC mechanisms.
With MULTIPLE BLOCKs, not OK:
 Cannot SYNC across multiple BLOCKs
 Data in Shared Memory is not persistent across kernel launches
Possible SOLUTION: EXTRA WORK per BLOCK

## Slide 62
Possible SOLUTION: EXTRA WORK per BLOCK
For this example, let each BLOCK compute extra elements on the borders with its neighboring BLOCKs. (see example on next slide)
For each additional iteration computed by the BLOCK, there is more REUSE of the elements copied from GLOBAL into SHARED memory.
However,
For each iteration, more border elements need to be loaded and computed which requires more transfers and more threads.
Break-even point depends on the work per BLOCK.

## Slide 63
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
IN | 25 | 6 | 34 | 91 | 10 | 62 | 55 | 5 | 80 | 20 | 10 | 40 | 6 | 99 | 26 | 2
1 | 25 | 22 | 44 | 45 | 54 | 42 | 41 | 47 | 35 | 37 | 23 | 19 | 48 | 44 | 42 | 2
2 | 25 | 30 | 37 | 48 | 47 | 46 | 43 | 41 | 39 | 32 | 26 | 30 | 37 | 45 | 29 | 2
3 | 25 | 31 | 38 | 44 | 47 | 45 | 43 | 41 | 37 | 32 | 29 | 31 | 37 | 37 | 25 | 2
4 | 25 | 31 | 38 | 43 | 45 | 45 | 43 | 41 | 40 | 33 | 31 | 33 | 35 | 33 | 21 | 2
 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
In | 5 | 80 | 20 | 10 | 40 | 6 | 99 | 26 | 2
1 | -- | 35 | 37 | 23 | 19 | 48 | 44 | 42 | 2
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
In | 25 | 6 | 34 | 91 | 10 | 62 | 55 | 5 | 80
1 | 25 | 22 | 44 | 45 | 54 | 42 | 41 | 47 | --
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
IN | 25 | 6 | 34 | 91 | 10 | 62 | 55 | 5 | 80 | 20
1 | 25 | 22 | 44 | 45 | 54 | 42 | 41 | 47 | 35 | --
2 | 25 | 30 | 37 | 48 | 47 | 46 | 43 | 41 | -- | --
 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
IN | 55 | 5 | 80 | 20 | 10 | 40 | 6 | 99 | 26 | 2
1 | -- | 47 | 35 | 37 | 23 | 19 | 48 | 44 | 42 | 2
2 | -- | -- | 39 | 32 | 26 | 30 | 37 | 45 | 29 | 2
Four iterations with a single BLOCK
One iteration with multiple BLOCKs requires ONE “border” element per neighbor
Two iteration with multiple BLOCKs requires TWO “border” elements per neighbor

## Slide 64
CODE SKETCH -- DOES NOT FULLY IMPLEMENT ALGORITHM
__global__ void kernel_avg_filter(float* x) {
const int tid = IMUL(blockDim.x, blockIdx.x) + threadIdx.x; // Assuming 1D block & 1D grid
const int local_tid = threadIdx.x; // Thread Id within the block
const int threadN = IMUL(blockDim.x, gridDim.x); // Assuming 1D block & 1D grid
float temp; int i;
// Number of threads = N / number of thread blocks; N = array length
__shared__ float xsm[THREADS_PER_BLOCK + 2*NUM_ITERS];
// Copy from the global memory to the shared memory
// Center
xsm[local_tid + NUM_ITERS] = x[tid];
//Left
if(local_tid < NUM_ITERS) {
xsm[local_tid] = x[NUM_ITERS + local_tid];
}
//Right
if(local_tid >= NUM_ITERS) {
xsm[local_tid + THREADS_PER_BLOCK] = x[NUM_ITERS + tid];
}
__syncthreads();
for(i = 0; i < NUM_ITERS; i++) {
// Compute the center elements
if (tid > 0 && tid < threadN-1) { // compute the average
temp = (xsm[local_tid + (NUM_ITERS-1)] + xsm[local_tid + (NUM_ITERS-1) + 1] +
xsm[local_tid + (NUM_ITERS-1) + 2]) / 3;
}
// Compute the left elements
// Compute the right elements
__syncthreads();
// Update the elements (center, left, right) in the shared memory
xsm[local_tid] = temp;
__syncthreads();
}
__syncthreads();
// Copy from the shared memory to the global memory
if (tid > 0 && tid < threadN-1) {
x[tid] = xsm[local_tid];
}
}

## Slide 65
//EXECUTABLE VERSION
// Define some constants
#define ARR_WIDTH 16
#define NUM_ITERS 4
#define NUM_BLOCKS 2
#define THREADS_PER_BLOCK (ARR_WIDTH/NUM_BLOCKS) + 2*NUM_ITERS
// This kernel assumes that each thread copies one array element from the global memory to
// the shared memory. This also includes copying the overlapping corner elements. That is
// why the number of threads = (work per block + 2*number of iterations). Then only some of
// the threads perform the actual computation and even fewer update the global memory.
__global__ void kernel_avg_filter(float* x, int arrLen) {
const int tid = IMUL(blockDim.x, blockIdx.x) + threadIdx.x;// Assume1D block and 1D grid
const int bid = blockIdx.x;
const int local_tid = threadIdx.x; // Thread Id within the block
const int threadN = IMUL(blockDim.x, gridDim.x); // Assuming 1D block and 1D grid
float temp;
int i;
int arr_id; //Index of the input array element for which this thread is responsible
int work_per_block;
// Threads per block = work per block + 2*NUM_ITERS
__shared__ float xsm[THREADS_PER_BLOCK];
work_per_block = (arrLen / NUM_BLOCKS);
arr_id = bid * work_per_block + (local_tid - NUM_ITERS);
// Copy from the global memory to the shared memory
// Leave out the first NUM_ITERS elements and the last NUM_ITERS elements
if(tid >= NUM_ITERS && tid < (threadN-NUM_ITERS)) {
xsm[local_tid] = x[arr_id];
}
__syncthreads();
for(i = 0; i < NUM_ITERS; i++) {
if (local_tid > 0 && local_tid < THREADS_PER_BLOCK-1) {
// Compute the average
temp = (xsm[local_tid - 1] + xsm[local_tid] + xsm[local_tid + 1]) / 3;
}
__syncthreads();
// Update only if computed
if (local_tid > 0 && local_tid < THREADS_PER_BLOCK-1) {
// and it is not the corner element of the original array
if (arr_id > 0 && arr_id < (arrLen-1)) {
xsm[local_tid] = temp;
}
}
__syncthreads();
}
__syncthreads();

## Slide 66
// Copy back from the shared memory to the global memory -- Only if the current thread
// was responsible to compute something and was also actually responsible to update
// the memory. (since some threads do repeat the computation for their local use but are
// not responsible to update the global memory).
if ((local_tid >= NUM_ITERS) && local_tid < (THREADS_PER_BLOCK-NUM_ITERS)) {
if (arr_id > 0 && arr_id < (arrLen-1)) {
x[arr_id] = xsm[local_tid];
}
}
}
// ---- Launch the kernel ---
kernel_avg_filter<<<NUM_BLOCKS, THREADS_PER_BLOCK>>>(d_my_x, ARR_WIDTH);